Architectural Specifications

The Installation Loop Driver shall continuously deliver 4.9 A (RMS) when excited with a continuous 1 kHz sine wave. It shall cover an area of at least 4,300 sqft. (400 m²) with a room aspect ratio 3:1 according to IEC 60118-4:2006 standard.  The driver shall have a frequency response of at least 80 Hz to 6.5 kHz +/- 3 dB with THD+N less than 0.2%.  The unit shall incorporate audio processing to maximize the intelligibility for individuals with a t-coil hearing aid.  The unit shall incorporate metal loss correction to rectify frequency caused adjacent metal structures.  The unit shall be wall mounted and all cables shall be terminated within the wall enclosure. The CLS2 Installation Loop Driver is specified.