Architectural Specifications

The field strength meter shall measure the background noise by determining the level of background magnetic field present in the intended location for the loop system. It shall measure the field strength delivered by the system. The meter shall measure the performance of the frequency spectrum required by IEC60118:2006 standard. It shall have an audio output to allow to the signal to be heard through a headphone or earspeaker. The meter shall include a LED graph with a wide view angle that is color coded. It shall accept two (2) AA alkaline batteries and display an illuminated LED when the battery is at acceptable level. The FSM Field Strength Meter is specified.