  - ASSISTIVE LISTENING SYSTEM

- Furnish and install a Hearing Loop assistive listening system for use by the hearing-impaired. The assistive listening system (ALS) shall cover the entire seating area. The ALS system shall conform to IEC 60118-4:2006 standards. Only Loop Drivers that meets measurement standards set forth in IEC 62489-1 shall be acceptable. Receivers shall be available in quantities required by the ADA. The receiver will incorporate a stereo headset jack that allows the user to plug in either a mono or stereo headset and listen to audio normally. The receivers shall incorporate automatic battery charging circuitry for recharging of Ni-MH batteries and incorporate a noise filter to reduce 60Hz hum. Listen Technologies Corporation products are specified.

- Qualification and Certification of the Contractor

Only AV Integration Firms/Dealers that have completed and are currently certified under specific manufacturer training to test, install, and commission along with providing a Certificate of Conformity in accordance with the IEC 60118-4 standard shall be eligible to bid upon this portion of this bid.

- Furnish and install the following:

  - Listen Technologies XX model Loop Driver (Qty: 1 ea.)

  - Listen Technologies LR-IRL-1 Loop receiver (Qty: XX ea.)

*The Americans with Disabilities Act (ADA) 2010 ADA Standards requires public facilities to provide auditory assistance devices.

http://www.ada.gov/regs2010/2010ADAStandards/2010ADAStandards.pdf

Section: 706 Assistive Listening Systems

Table 219.3 Receivers for Assistive Listening Systems

| Capacity of Seating in Assembly Area | Minimum Number of Required Receivers *contact Listen for customized quote to accommodate area sales@listentech.com www.listentech.com | Minimum Number of Required Receivers Required to be Hearing-aid Compatible (not required with induction loop systems) |
| --- | --- | --- |
| 50 or less | 2 | 2 |
| 51 to 200 | 2, plus 1 per 25 seats over 50 seats* | 2 |
| 201 to 500 | 2, plus 1 per 25 seats over 50 seats* | 1 per 4 receivers* |
| 501 to 1000 | 20, plus 1 per 33 seats over 500 seats* | 1 per 4 receivers* |
| 1001 to 2000 | 35, plus 1 per 50 seats over 1000 seats* | 1 per 4 receivers* |
| 2001 and over | 55 plus 1 per 100 seats over 2000 seats* | 1 per 4 receivers* |

*Or fraction thereof