Architectural Specifications

The audio hearing loop driver shall continuously deliver 3.4 A (RMS) when excited with a 1 KHz sine wave. It shall cover an area of at least 2,150 sqft. (200 m²) with a room aspect ratio 3:1 according to IEC 60118-4:2006 standard. The driver shall have a frequency response of at least 80 Hz to 6.5 KHz – 3 dB with THD+N less than 0.5%.  The unit shall incorporate audio processing to maximize the intelligibility for individuals with a t-coil equipped hearing aid.  The unit shall incorporate 2 microphone inputs, 1line input, tone control and voice controlled switching (VOX).  The ILD100DC Professional Loop Driver is specified.