Architectural Specifications

The audio hearing loop driver shall continuously deliver 4.9 A (RMS) when excited with a continuous 1 kHz sine wave. It shall cover an area of at least 4,450 sqft. (31 m²) with a room aspect ratio 3:1 according to IEC 60118-4:2006 standard.  The driver shall have a frequency response of at least 80 Hz to 6.5 kHz +/- 3 dB with THD+N less than 0.2%.  The unit shall incorporate audio processing to maximize the intelligibility for individuals with a t-coil equipped hearing aid.  The unit shall incorporate metal loss correction to rectify frequency caused adjacent metal structures.  The unit shall occupy one-half rack space.  The ILD300 Professional Loop Driver (4.9 Amps) is specified.