Architectural Specifications

The audio hearing loop driver shall continuously deliver 6.4 A (RMS) when excited with a continuous 1 kHz sine wave. It shall cover an area of at least 7530 sqft. (700 m²) with a room aspect ratio 3:1 according to IEC 60118-4:2006 standard.  The driver shall have a frequency response of at least 80 Hz to 6.5 kHz +/- 3 dB with THD+N less than 0.2%.  The unit shall incorporate audio processing to maximize the intelligibility for individuals with a t-coil equipped hearing aid.  The unit shall incorporate metal loss correction to rectify frequency caused adjacent metal structures.  The unit shall occupy one rack space and rack mount brackets shall be included.  The ILD500 Professional Loop Driver is specified.