  - ASSISTIVE LISTENING SYSTEM

- Furnish and install an FM wireless assistive listening system for use by the hearing-impaired. The assistive listening system (ALS) shall be capable of broadcasting on 57 channels and be frequency agile. The ALS system shall have 80dB SNR or greater, end-to-end. Receivers shall be frequency agile and frequency set with a "seek" button. The receiver will incorporate a stereo headset jack that allows the user to plug in either a mono or stereo headset and listen to audio normally. The portable receivers and transmitters shall incorporate automatic battery charging circuitry for recharging of Ni-MH batteries. Listen Technologies Corporation products are specified.

- Furnish and install the following:

  - Listen Technologies LT-800-072 Base Transmitter (Qty: 1 ea.)

  - Listen Technologies LA-326 Rack mount kit (Qty: 1 ea.).

  - Listen Technologies LA-122 Universal antenna. (Qty: 1 ea.) Mount as needed, can be mounted on ceiling, wall, and remote base or flexible dipole. If antenna is remoted use RG58 for less than 100ft or RG8 for more than 100ft runs (50 0hm).

  - Listen Technologies LR-400-072 Portable Display receiver (Qty: 2 each or as needed, see note*)

  - Listen Technologies LA-164 Ear Speaker (Qty: 2 ea.)

  - Listen Technologies LA-166 Neckloop.  (Qty: 2 ea.)

  - Listen Technologies LA-321 8 unit charging carrying case. (Qty: 1 ea.)

  - Listen Technologies LA-362 Ni-MH rechargeable batteries (Qty: 4 ea.)

  - Listen Technologies LA-304 ADA Access/Compliance signage kit. (Qty 1 ea.)

*The Americans with Disabilities Act (ADA) 2010 ADA Standards requires public facilities to provide auditory assistance devices.

http://www.ada.gov/regs2010/2010ADAStandards/2010ADAStandards.pdf

Section: 706 Assistive Listening Systems

Table 219.3 Receivers for Assistive Listening Systems

| Capacity of Seating in Assembly Area | Minimum Number of Required Receivers *contact Listen for customized quote to accommodate area sales@listentech.com www.listentech.com | Minimum Number of Required Receivers Required to be Hearing-aid Compatible (using Listen LA-166) |
| --- | --- | --- |
| 50 or less | 2 | 2 |
| 51 to 200 | 2, plus 1 per 25 seats over 50 seats* | 2 |
| 201 to 500 | 2, plus 1 per 25 seats over 50 seats* | 1 per 4 receivers* |
| 501 to 1000 | 20, plus 1 per 33 seats over 500 seats* | 1 per 4 receivers* |
| 1001 to 2000 | 35, plus 1 per 50 seats over 1000 seats* | 1 per 4 receivers* |
| 2001 and over | 55 plus 1 per 100 seats over 2000 seats* | 1 per 4 receivers* |

*Or fraction thereof