  - ASSISTIVE LISTENING SYSTEM

- Furnish and install an FM wireless assistive listening system for use by the hearing-impaired. The assistive listening system (ALS) shall be capable of broadcasting on 3 wide band channels and be frequency agile. The ALS system shall have 62dB SNR or greater, end-to-end. Receivers shall be frequency agile to 3 wide band frequencies set with a “channel select” switch.  The receivers will incorporate a stereo headset jack that allows the user to plug in either a mono or stereo headset and listen to audio normally. The receivers shall offer 120 hours of battery like on alkaline batteries.  The receivers and transmitters shall offer a limited lifetime warranty.  Listen Technologies Corporation LP-3CV-072-01 products are specified.

- Furnish and install the following:

  - Listen Technologies LT-803-072 Stationary 3-Channel FM Transmitter (Qty: 1 ea.)

  - Listen Technologies LR-200-072 Standard 3-Channel FM receiver (Qty: 4 each or as needed, see note*)

  - Listen Technologies LA-161 Ear Bud (Qty: 4 ea.)

  - Listen Technologies LA-362 NiMH rechargeable batteries. (Qty: 8 ea.)

  - Listen Technologies LA-321-01 8-Unit Charging/Carrying Case (Qty 1 ea.)

*The Americans with Disabilities Act (ADA) 2010 ADA Standards requires public facilities to provide auditory assistance devices.

http://www.ada.gov/regs2010/2010ADAStandards/2010ADAStandards.pdf

Section: 706 Assistive Listening Systems

Table 219.3 Receivers for Assistive Listening Systems

| Capacity of Seating in Assembly Area | Minimum Number of Required Receivers *contact Listen for customized quote to accommodate area sales@listentech.com www.listentech.com | Minimum Number of Required Receivers Required to be Hearing-aid Compatible (using Listen LA-166) |
| --- | --- | --- |
| 50 or less | 2 | 2 |
| 51 to 200 | 2, plus 1 per 25 seats over 50 seats* | 2 |
| 201 to 500 | 2, plus 1 per 25 seats over 50 seats* | 1 per 4 receivers* |
| 501 to 1000 | 20, plus 1 per 33 seats over 500 seats* | 1 per 4 receivers* |
| 1001 to 2000 | 35, plus 1 per 50 seats over 1000 seats* | 1 per 4 receivers* |
| 2001 and over | 55 plus 1 per 100 seats over 2000 seats* | 1 per 4 receivers* |

*Or fraction thereof