  - IR ASSISTIVE LISTENING SYSTEM

- Furnish and install an Infra-Red (IR) wireless assistive listening system. The assistive listening system (ALS) shall be capable of broadcasting mono or stereo channels on up to 4 Upper Band IR carrier frequencies. Stethoscope or Lanyard style IR Receivers shall be frequency agile and frequency set with a push button channel selector. The Lanyard style receivers will incorporate a stereo headset jack that allows the user to plug in a stereo headset. The receivers shall incorporate automatic signal mute or squelch when no IR signal is received. Receivers shall be powered by either   standard AAA batteries offering up to 30 hours of use or NiMH battery packs offering up to 15 hours of use. Use of NiMH battery packs will require a recharging station. IR radiators shall come in Grey or White, have all needed hardware for mounting on wall, ceiling, table-top or mic stand and have auto-off feature to preserve LED life. Listen Technologies Corporation products are specified.

- Furnish and install the following:

  - Listen Technologies LT-82 Stationary IR Transmitter. (Qty: 1 ea.).

  - Listen Technologies LA-326 Rack mount kit (Qty: 1 ea.).

  - Listen Technologies LA-140 IR Radiator. Mount as needed, can be mounted on ceiling, wall, remote base or mic stand. Radiator comes complete with 2 each 25ft. RG58 50 Ohm coaxial and CAT5 cables. (Qty: 1 ea. Or as needed see note*)

  - Listen Technologies LR-42 IR Stetho 4 channel receiver (Qty: 2 each or as needed, see note**)

  - Listen Technologies LR-44 IR Lanyard 4 channel receiver (Qty: 2 each or as needed, see note**)

  - Listen Technologies LA-165 Stereo Headphones (Qty: 2 ea.)

  - Listen Technologies LA-166 Neck-loop.  (Qty: 1 ea.)

  - Listen Technologies LA-350 8 unit charging station. (Qty: 1 ea.)

  - Listen Technologies LA-364 Ni-MH rechargeable battery packs (Qty: 4 ea.)

  - Listen Technologies LA-304 ADA Access/Compliance signage kit. (Qty 1 ea.)

* Each LA-140 IR radiator covers approximately 10,000 square feet for a mono channel.

*The Americans with Disabilities Act (ADA) 2010 ADA Standards requires public facilities to provide auditory assistance devices.

http://www.ada.gov/regs2010/2010ADAStandards/2010ADAStandards.pdf

Section: 706 Assistive Listening Systems

Table 219.3 Receivers for Assistive Listening Systems

| Capacity of Seating in Assembly Area | Minimum Number of Required Receivers *contact Listen for customized quote to accommodate area sales@listentech.com www.listentech.com | Minimum Number of Required Receivers Required to be Hearing-aid Compatible (using Listen LA-166) |
| --- | --- | --- |
| 50 or less | 2 | 2 |
| 51 to 200 | 2, plus 1 per 25 seats over 50 seats* | 2 |
| 201 to 500 | 2, plus 1 per 25 seats over 50 seats* | 1 per 4 receivers* |
| 501 to 1000 | 20, plus 1 per 33 seats over 500 seats* | 1 per 4 receivers* |
| 1001 to 2000 | 35, plus 1 per 50 seats over 1000 seats* | 1 per 4 receivers* |
| 2001 and over | 55 plus 1 per 100 seats over 2000 seats* | 1 per 4 receivers* |

*Or fraction thereof