  - HEARING LOOP SYSTEM

- Furnish and install a Hearing Loop assistive listening system for use by the hearing-impaired. The MultiLoop driver shall continuously deliver two (2) x 9.2 A (RMS) per channel when excited with a 1 kHz sine wave as measured with the IEC 62489-1 induction loop amplifier performance standard.  Only drivers that have been tested and compliant to this IEC 62489-1 specification shall be accepted, no other substitutions will be allowed.

In a Perimeter Loop application it shall cover up to two (2) x 13,990 sq. ft. (1,300 m²) each.  In a MultiLoop Low Loss or, Low Spill Phased Array application it shall cover up to 35,520 sq. ft. (3,300 m²). The MultiLoop driver shall internally incorporate two (2) loop drivers and one (1) SP5 90° audio phase shifter. The MultiLoop driver with the proper design shall have reduced spill to no more than 1.5 ft. (1 m).  The MultiLoop driver shall have a frequency response of at least 80Hz to 6.5kHz +/- 3 dB with THD+N less than 0.2%. The unit shall incorporate (AGC) Audio Gain Control optimized for speech with a compression dynamic range of >36 dB audio processing. The unit shall incorporate Metal Loss Correction to rectify frequency loss caused adjacent metal structures.  The unit shall occupy one rack space and rack mount brackets shall be included.  The MultiLoop driver is tested to and compliant with: IEC 62489-1 induction loop amplifier performance standard.

The MLD9 MultiLoop™ Driver (9.0A) is specified.

Qualification and Certification of the Contractor

Only AV Integration Firms/Dealers that have completed and are currently certified under specific manufacturer training to test, install, and commission along with providing a Certificate of Conformity in accordance with the IEC 60118-4 standard shall be eligible to bid upon this portion of this bid.

Listen Technologies Corporation products are specified.

- Furnish and install the following:

  - Listen Technologies MLD9 MultiLoop™ Driver (Qty: x ea.)

  - Listen Technologies LP-IL-1 Hearing Loop Receiver with Lanyard Package (Qty: *TBD)  *NOTE:  Please refer to the Table 219.3 for required number of receivers under the ADA 2010 requirements.  The “Hearing Aid Compatible” quantity and column doesn’t apply to Hearing Loop systems.

*The Americans with Disabilities Act (ADA) 2010 ADA Standards requires public facilities to provide auditory assistance devices.

http://www.ada.gov/regs2010/2010ADAStandards/2010ADAStandards.pdf

…Continued

Section: 706 Assistive Listening Systems

Table 219.3 Receivers for Assistive Listening Systems

| Capacity of Seating in Assembly Area | Minimum Number of Required Receivers *contact Listen for customized quote to accommodate area sales@Listentech.com www.listentech.com | Minimum Number of Required Receivers Required to be Hearing-aid Compatible (using Listen LA-166) |
| --- | --- | --- |
| 50 or less | 2 | 2 |
| 51 to 200 | 2, plus 1 per 25 seats over 50 seats* | 2 |
| 201 to 500 | 2, plus 1 per 25 seats over 50 seats* | 1 per 4 receivers* |
| 501 to 1000 | 20, plus 1 per 33 seats over 500 seats* | 1 per 4 receivers* |
| 1001 to 2000 | 35, plus 1 per 50 seats over 1000 seats* | 1 per 4 receivers* |
| 2001 and over | 55 plus 1 per 100 seats over 2000 seats* | 1 per 4 receivers* |

*Or fraction thereof