  - iDSP ASSISTIVE LISTENING SYSTEM

- The stationary RF transmitter shall be capable of broadcasting on 57 channels. The transmitter shall have an SNR of 80 dB or greater. The output power shall be adjustable to quarter, half or full. Channel tuning shall be capable of being locked. The device shall have an audio frequency response of 50 Hz to 15k Hz, ±3 dB at 72 MHz. It shall have two (2) mixing audio inputs and a mixed signal output. The device shall have the following audio controls: input level, mix level and an adjustable low pass filter (contour). The device shall have an audio processor that is capable of automatic gain control and limiting. The Listen Technologies LT-800-072 is specified.

- The RF receiver shall be capable of receiving on 57 wide and narrow band channels. The device shall tune to a single channel and user shall not be able to change the channel. The receiver shall have an audio frequency response of 50 Hz - 15 kHz (±3 dB). The device shall have the option of worn on a lanyard or belt clip and the lanyard shall have the option of an integrated DSP driven neck loop that automatically senses and sends optimized audio signals directly to telecoils. The ALS system shall have 80dB SNR or greater, end-to-end. The Listen Technologies LR-4200-072-P1 is specified.

Furnish and install an RF wireless assistive listening system+.

  - Listen Technologies LT-800-072 Base Transmitter (Qty: 1 ea.)

  - Listen Technologies LA-326 Rack mount kit (Qty: 1 ea.)

  - Listen Technologies LA-122 Universal Antenna Kit. (Qty: 1 ea.)

  - Listen Technologies LR-4200-072-P1 Intelligent DSP RF Receiver Package, 72MHz (Qty: 4 each or as needed, see calculator*) Package Includes: LR-4200 iDSP Receiver, LA-401 Universal Ear Speaker, LA-430 Intelligent Earphone/Neck Loop Lanyard, and LA-365 Rechargeable Li-Ion Battery.

  - Listen Technologies LA-381 Intelligent 12 Unit Charging Tray (Qty: 1 ea. or as needed)

  - Listen Technologies LA-304 ADA Access/Compliance signage kit. (Qty: 1 ea.)

+The Americans with Disabilities Act (ADA) 2010 ADA Standards requires public facilities to provide auditory assistance devices. http://www.ada.gov/regs2010/2010ADAStandards/2010ADAStandards.pdf

*Calculator: http://www.listentech.com/support/ada-info/ada-tools-kits/