2.01 Assistive Listening System – Infrared System

- Transmitter/Radiator Combo

The Infrared Transmitter/Radiator Combo shall be capable of broadcasting up to two (2) audio channels with the choice of four (4) mono carrier frequencies; 2.3, 2.8, 3.3, and 3.8 MHz. Channel carrier selections shall be set via a back panel rotary switches. The Transmitter/Radiator coverage area shall be up to 30,000 ft² (2787 m²) with single channel transmission when using the LR-5200-IR. The device shall have a timer that shuts off the carriers after 15 minutes when no audio is present at the inputs. The device shall have two (2) independent mixing audio inputs, one for each transmission channel. The Transmitter/Radiator shall provide both power and audio signal for up to Four (4) Expansion Radiators over CAT-5e cable. The Listen Technologies LT-84 is specified.

- LR-5200 -IR Advanced Intelligent DSP IR Receiver

The IR receiver shall be capable of receiving on four (4) wide band channels (carriers), Channel 1, 2, 3, and 4  (2.3, 2.8, 3.3, and 3.8 MHz respectively). The device shall have a programmable multi-function Listen button that can be tuned for the venues desired channels and electronically lock out any unused channels. The receiver shall have the option of being lanyard or belt clip worn and the lanyard shall incorporate an integrated neck loop for compatibility with T-coil hearing aids. The receiver shall be covered by a hassle free limited lifetime warranty. The Listen Technologies LR-5200-IR-P1 is specified.

Furnish and install an IR wireless assistive listening system+

- Listen LT-84 Listen IR Transmitter/Radiator Combo (1) Includes: Power Supply/Cord, Flexible Mounting Hardware, Phoenix type connectors, and Multi-Lingual Assistive Listening  Signage Kit

- Listen Technologies LR-5200-IR-P1 Advanced Intelligent DSP IR Package, (Qty: 4 each or as needed, see calculator*). Package Includes: LR-5200-IR iDSP Receiver, LA-401 Universal Ear Speaker, LA-430 Intelligent Neck Loop Lanyard, and LA-365 Rechargeable Li-Ion Battery

- Listen LA-381-01 Intelligent 12-Unit Charging Tray (Qty: 1 ea. or as needed)

- Listen LA-422 USB to Micro USB Programming Cable

+The Americans with Disabilities Act (ADA) 2010 ADA Standards requires public facilities to provide auditory assistance devices. http://www.ada.gov/regs2010/2010ADAStandards/2010ADAStandards.pdf

*Calculator http://www.listentech.com/support/ada-info/ada-tools-kits/