  - Wireless Audio Distribution System

- Furnish and install a stationary RF wireless audio distribution system. The system shall be capable of broadcasting on 57 channels and be frequency agile. The system shall have 80dB SNR or greater, end-to-end. Receivers shall be rack mountable, frequency set with a "seek" button or up/down digital tuning method with LCD display to verify channel, RF strength and channel lock status. The receiver will incorporate a 15 watt power amplifier, audio output/auxiliary audio input connections, level controls for the RF & aux inputs, adjustable squelch, and offer 120V AC or 12 VDC operation. Listen Technologies products are specified.

- Furnish and install the following:

  - Listen Technologies LT-800-216 Base Transmitter (Qty: 1 ea.)

  - Listen Technologies LA-326 Rack mount kit (Qty: 3 ea.).

  - Listen Technologies LA-107 Weatherized Dipole 216 Mhz antenna. (Qty: 3 ea.) Mount as needed on mast outdoors; use RG58 for less than 100ft. or RG8 for more than 100ft. runs (50 0hm).

  - Listen Technologies LR-100-216 Stationary Receiver / Power Amplifier (Qty. 2 or as needed).