  - ASSISTIVE LISTENING SYSTEM TO MEET ADA

- Furnish and install a RF wireless assistive listening system (ALS) +. The ALS shall be capable of broadcasting on 3 wide band channels and be frequency agile. The ALS system shall have 62dB SNR or greater, end-to-end. Receivers shall be frequency agile to 3 wide band frequencies set with a “channel select” switch. The receivers will incorporate a stereo headset jack that allows the user to plug in either a mono or stereo headset and listen to audio normally. The receivers shall offer 120 hours of battery like on alkaline batteries. The receivers and transmitters shall offer a limited lifetime warranty. Listen Technologies products are specified.

Furnish and install the following:

  - Listen Technologies LP-3CV-072-01. System includes: (1) LT-803-072 Stationary 3-Channel FM Transmitter, (1) LA-123 90° Helical Antenna, (4) LR-200-072 3-Channel FM Receivers, (4) LA-161 Single Ear buds, and (1) LA-304 Assistive Listening Signage Kit

  - Listen Technologies LA-321-01 8-Unit Charging/Carrying Case (Qty 1 ea.)

  - Listen Technologies LA-166 Neck Loop (*Qty 2 each or as needed, see calculator)

  - Listen Technologies LR-200-072 Receivers, (*Additional as needed, see calculator)

  - Listen Technologies LA-164 Ear Buds, (*Additional as needed, see calculator)

  - Listen Technologies LA-362 NiMH rechargeable batteries (as needed)

+The Americans with Disabilities Act (ADA) 2010 ADA Standards requires public facilities to provide auditory assistance devices. http://www.ada.gov/regs2010/2010ADAStandards/2010ADAStandards.pdf

*Calculator: http://www.listentech.com/support/ada-info/ada-tools-kits/